## Slide 1: Coilover Damping Adjusters
Started: 8/10/2022

## Slide 2: High Level Block Diagram (old) – 8/10/2022
OLED Display
Encoder for user input
IIC Master for communicating with motors
Main Control Board
IIC Slave
Stepper Motor and Driver
Encoder for Motor Position Feedback
Stepper Motor Board
IIC Slave
Stepper Motor and Driver
Encoder for Motor Position Feedback
Stepper Motor Board
IIC Slave
Stepper Motor and Driver
Encoder for Motor Position Feedback
Stepper Motor Board
IIC Slave
Stepper Motor and Driver
Encoder for Motor Position Feedback
Stepper Motor Board
*Notes
IIC daisy chained to minimize the amount of wire.

## Slide 3: Motor Control Board Block Diagram – 8/13/22
ATtiny3217
or
AVR32DA32
DRV8825
NEMA-17 Short Stepper Motor
Coilover Damping Adjustment Screw
Bours open-center encoder
IIC Master

## Slide 4: PCB Board Cutout Coordinates – 8/19/22
(100,100)
Coordinates of each corner relative to origin (100, 100)

## Slide 5: Controller Board Block Diagram
ATUC128D3
or
SAM4LC2BA
240x320
LCD
ST7789
or variant
FL
RL
RR
FR
Stepper Motor Boards
8-bit parallel interface
Serial EEPROM
Switches

## Slide 6: High Level Block Diagram Updated – 9/22/22
Power Board
Located by fuse box.
4x Connectors for power and communication.
12V
GND
IIC Slave
Stepper Motor and Driver
Encoder for Motor Position Feedback
Stepper Motor Board Front Right
IIC Slave
Stepper Motor and Driver
Encoder for Motor Position Feedback
Stepper Motor Board Front Left
IIC Slave
Stepper Motor and Driver
Encoder for Motor Position Feedback
Stepper Motor Board Rear Right
IIC Slave
Stepper Motor and Driver
Encoder for Motor Position Feedback
Stepper Motor Board Rear Left
LCD Display
Switches for user input
IIC Master for communicating with motors
Main Controller
Operated by driver

## Slide 7: Top of Strut Dimensions and Actuator Depth – 10/9/22
Optimal length for hex key: 20.5mm from start of mounting (female) threads.

## Slide 8: Encoder Filtering – 8/14/22
Encoder max current rating: 10mA @ 5v
  Pull-up resistor for 10mA @ 3.3V: >=330 ohm
Max stepper RPM: ~100 rpm
  Encoder pulses per rotation (PPR): 10
  Pulses per second: 16.67
  Min cutoff frequency: 16.67 Hz
R1 = 330
R2 = 7.5k
C1 = 1u
  Fc_open = 20.32 Hz
  Fc_closed = 21.22 Hz
If R2 = 5.1k
  Fc_open = 29.31 Hz
  Fc_closed = 31.21 Hz

## Slide 9: Encoder Filtering Cont – 8/15/22
Schmitt trigger max upper threshold @ 3V: 2.0V
Schmitt trigger min lower threshold @ 3V: 0.8V
RC filter output with R2 = 5.1k
RC Filter output with R2 = 7.5k

## Slide 10: Stepper Current Sense Loop – 8/19/22
ATtiny32xx DAC output range: 0.2 to VDD-0.2
AVR32 DAC output range: GND to VDD
DVR8825 Vref absolute range: 0V – 3.5V
  Recommended range: 1V – 3.5V
Rsense: 0.1 ohm
Vref for 1A Ichop: 0.5V
Rsense power dissipation: 0.1W
Rsense: 0.25 ohm
Vref for 1A Ichop: 1.26V
Rsense power dissipation: 0.251W

## Slide 11: Stepper Motor Current Loop – 8/21/22
Goal is to keep current loop as short and constrained as possible.
Peak current of 1A per coil

## Slide 12: On-Board Voltage Measurements – 8/21/22
Vref = 2.5V
Battery Voltage
Max battery voltage: 15V
Min battery voltage: 11V
R1 = 1200, R2 = 200 -> divide by 7
  Max power = 160.7mW
Max divider output = 2.143V = 3511 (12 bit output)
Min divider output = 1.571V = 2574 (12 bit output)
Battery Voltage = ADC result / 1638.4
Vref = 2.5V
Regulated Voltage
Max, hopefully, 3.3V
Min, because of Vref, 2.5V
R1 = 680, R2 = 680 -> divide by 2
  Max power = 165.4mW
Max divider output = 1.65V = 2703 bits
Min divider output = 1.25V = 2048 bits
Regulated Voltage = ADC result / 1638.4

## Slide 13: On-Board Voltage Measurements – 9/1/22
Calculating minimum impedance divider while not exceeding resistor power rating (0.25W)

## Slide 15: Mounting – 8/26/22
Coilover top hat thread size M12x1.25

## Slide 16: Controller MCU Selection – 8/29/22
Device/Description | # of pins
LCD data pins | 8
LCD backlight | 1
LCD Data/Cmd, CS, RD, WR | 4
LCD reset | 1
At least 1 IIC | 2
Buttons | >=5
Total | >=21 + prog pins
Minimum memory:
  Absolutely no less than 128kB, ideally more than or equal to 256kB.
Peripherals:
  At least 1 IIC.
  CANBUS for future use.
  EMI/SBC?
ATSAM4LC2BA

## Slide 17: ATSAM4LC2BA Clocking – 9/1/22
Crystal: AS-30.000-10-F-2020-EXT-SMD-TR
External capacitor value =
Cx = 2(CL – Cstray) = 2(10pF – 3pF) = 14pF

## Slide 18: Controller Board Buttons Filter – 9/2/22
Max current through button: 10mA
  Pull resistor (R21): 3.3V / 10mA = 330 ohm
Cutoff frequency minimum: 15Hz
  fc,min = 1 / ((2*pi)*(R21+R22)*C16)
C16: 1uF
R21: 330
R22: 10k
Switch pressed cutoff frequency = 15.92Hz
Switch released cutoff frequency = 15.41Hz

## Slide 19: ATUC128D3 Clocking – 9/3/22

## Slide 20: DRV8825 Step PWM Frequency Calculation – 9/15/22

## Slide 21: Stepper Motor Timeout Frequency Calculations – 10/7/2022

## Slide 22: UPDI Pinout – 8/13/22
Atmel ICE Pinout
My Pinout

## Slide 23: UPDI Pinout - 8/20/22
Updated schematic for AVR32DA32

## Slide 24: UA78M33CKVURG3 Footprint – 8/15/22
Had to modify existing KiCAD TO-252 footprint. Extended pin 1 & 3 pads to 2.75mm from 2.2mm.

## Slide 25: ATSAM4LC2BA JTAG Pinout – 8/30/22

## Slide 26: ATSAM4LC2BA I2C Pins – 8/31/22

## Slide 27: BSR802N Backlight FET Pinout – 9/1/22
Datasheet

## Slide 28: ATUC128C3 JTAG Pinout – 9/3/22

## Slide 29: SN74LVC2G17 Decoupling – 8/15/22

## Slide 30: UA78M33CKVURG3 Decoupling – 8/17/22

## Slide 31: AVR32DA32 Decoupling

## Slide 32: ATSAM4LC2BA Power Supply – 8/30/22
VDDANA, GNDANA
  Analog Voltage Supply,
  3.3V
VDDCORE
  Core voltage supply
  1.8V, connect to VDDOUT
VDDIN
  Voltage regulator in
  3.3V
VDDIO
  IO Voltage,
  3.3V,
VDDOUT
  Voltage regulator output
  1.8V out